## Slide 1
Hydrogen: Fuel
Proposal:
Use hydrogen gas as a fuel. It has a high energy density and the only product when it burns is water.
2H2(g) + O2(g)  2H2O(l)
ΔH = -282 kJ mol-1
© POShea

## Slide 2
Generate hydrogen
Blend it with natural gas
Use it in vehicles
Export it.

## Slide 3
Question:
How to source hydrogen?
Latrobe Valley trial: hydrogen from coal using steam reforming.
CH4(g) + H2O(g)  CO(g) + 3H2(g)
CO(g) + H2O(l)  CO2(g) + H2(g)
Problem: produces CO2

## Slide 5
Solar option
WA trial. Electrolysis of water using solar array.
2H2O(l)  2H2(g) + O2(g) Pollution free
Supply of water and electricity required.

## Slide 6
Anode: 2H2(g)  2H+(aq) + 2e
Cathode: O2(g) + 4H+(aq) + 4e  2H2O(l)
Overall: 2H2(g) + O2(g)  2H2O(l)
Hydrogen fuel cell:
generating electricity from hydrogen
Expensive: high tech porous electrodes

## Slide 7
Adelaide trial: water to hydrogen. Hydrogen blended with natural gas to be used in surrounding homes.

## Slide 8
South Australian trial:
convert hydrogen to ammonia for fertiliser or as a safe means of transport.

## Slide 9
Ammonia production
N2(g) + 3H2(g) ⇌ 2NH3(g)
This is the Haber process.

## Slide 10
N2(g) + 3H2(g) ⇌ 2NH3(g)
The above reaction is reversed once ammonia has been transported.
CSIRO has invented a membrane to absorb hydrogen gas. As stated by Le Chatelier, removing hydrogen will favour the reverse reaction.