## Slide 1
Polypropene
(Polypropylene)
© POShea

## Slide 2
Propene reacts with itself to form polypropene.
Addition polymerisation.
Polymer pellets – ready for moulding.

## Slide 3
Polypropene items: Cheaper polymer with superior toughness and melting point to polyethene.
Identified as recycle code 5.

## Slide 4
Many medical packaging uses.
Also used for
Carpet and rugs: durable, colourfast fibres
Microwave food containers, plates and kitchen items: oil and bacteria resistance
Luggage: backpacks, suitcases and shopping bags

## Slide 5
Playing surface and seats both made from polypropene.

## Slide 6
Polypropene variations
The properties will differ depending upon how the methyl side chains orient.

## Slide 7
Atactic
Methyl groups are randomly positioned on either side of the chain.

## Slide 8
Isotactic
Methyl groups all on the same side
Syndotactic
Methyl groups alternating
Symmetry in a structure allows tight packing of molecules.
Tight packing increases crystallinity , increasing hardness, brittleness and melting point.

## Slide 9
Ziegler-Natta catalysts: allow control of the placement of each monomer.

## Slide 10
Bio-polypropene.
The monomer can be sourced from bioethanol or biopropan-2-ol.

## Slide 11
Copolymer with smaller percentages of ethene.
The presence of ethene disrupts the symmetry of the structure.
Copolymer is less crystalline and will be more transparent and have a lower melting point.

## Slide 13
Three monomers – propene, ethene and but-1-ene.
Increased transparency

## Slide 14
Where does the propene come from?
It is formed as a byproduct when ethane is cracked to ethene at Qenos.
C2H6(g) ⇌C2H4(g) + H2(g)
Cracking is conducted under very harsh conditions, high temperature and very high pressure.
Propene is separated from ethene by fractional distillation.