## Slide 1
Qenos: Altona
Polyethene manufacture ©POShea

## Slide 2
Qenos is a large petrochemical plant in Altona that makes polyethene from ethene using petroleum feedstock.

## Slide 3
Qenos: ethane feedstock converted to ethene (ethylene).
Ethene is then polymerised to polyethene

## Slide 4
Cracker
C2H6(g) ⇌ C2H4(g) + H2(g) endothermic
A difficult reaction – harsh conditions used.
temperatures up to 9000C (T goes up, K goes up)
a very short reaction time
low hydrocarbon concentrations (favours forward reaction; 1:2 reactant to product ratio)
rapid cooling of products to prevent their decomposition. (K value higher at low temp)
Ethane to ethene:
Cracking of an alkane to an alkene

## Slide 5
Twin cracking units –
- maintenance on one, the other still runs.

## Slide 6
Ethane supply
Ethane is obtained by fractional distillation of gas from the Gippsland gas fields or from overseas crude oil. Pipelines from the refineries supply Qenos

## Slide 7
Polymerisation
Polyethene
Ethene
Addition polymerisation

## Slide 8
LDPE: low density polyethene
Polymerisation at high pressure and temperature produces an untidy, branched structure. The chains do not pack neatly so it is called low density polyethene.

## Slide 9
LLDPE: linear low density polyethene
If a high-tech Ziegler-Natta catalyst is used, high pressure and temperature are not needed and the polymer structure is linear.

## Slide 10
The branches in LLDPE are not caused during polymerisation, they are due to small amounts of but-1-ene monomer being included in the structure. The small branch is the rest of the butene molecule..

## Slide 11
LLDPE is sold as pellets. Manufacturers heat these pellets and add colour to make a range of commercial products.

## Slide 12
http://www.qenos.com/internet/home.nsf/web/RHAT-9AZ9JC
https://www.newmac.co/portfolio/qenos-transformation-video/
Qenos have named the LLDPE they use for milk containers, Alkatane.